## Slide 1: Design of a 4-bit Computer in VerilogHDL
With a fixed instruction set
Prepared By:
Shafin Bin Hamid
ID: 1606008
Video Link: https://web.microsoftstream.com/video/dbf29407-a455-41e4-a275-d2d4b0443ec8?list=studio

## Slide 2: Outline
A Progressive Route (From SAP-1 to My own design)
Unique Features of the Design
Demonstration using a sample testbench program

## Slide 3: A progressive route(From SAP-1 to my own design)
Build a SAP-1 from scratch
Gradually add parts to it for handing more complex instructions
Temporary Register
Flags
Register

## Slide 4: A progressive route(From SAP-1 to my own design)
Testbench
Program Counter Testbench
MAR Testbench
RAM Testbench

## Slide 5: A progressive route(From SAP-1 to my own design)
Build a Control Sequencer to generate control signals for synchronization
Control Sequencer is the brain of the computer because it controls which modules are active/inactive
Control signals are generated at the negedge
The operation based on the control signal happens on the next posedge
Need to make all the modules work synchronously
So everything happens as and when they are required to do so

## Slide 6: Final Design
RAM Size is 16 * 8
First 9 locations contain instructions
Next 5 locations are for storing data
Last 2 locations are stack memory
Instruction length is 8 bits
Data length is 4 bits
For data, first 4 bits are set to zero
First 4 bits of instruction are opcode, second 4 bits are operand
For instructions that do not have a valid operand, last 4 bits are set to zero
All ALU operations are done with 4-bit registers

## Slide 7: Unique Features of the Design
No common ‘Write BUS’
Communications between different modules are established through separate buses
There is one bus connecting PC to MAR and there is another bus connecting IR to MAR etc
No unwanted overwrites
Increased reliability
Easy to understand for one-way bus communication
Synchronous operation

## Slide 8: Demonstration of the Computer
A sample testbench code
Declaration of all the control signals along with the buses between different modules
Common clock and reset

## Slide 9: Demonstration of the Computer
A sample testbench program
Instantiation of all modules

## Slide 10: Demonstration of the Computer
A sample testbench program
MOV A,9h ;move RAM[9] to A
XCHG A,B ;swap A and B
MOV A, Ah ;move RAM[10] to A
PUSH B ;Push B to stack
SHR A ;shift logical right A by one bit
HLT ;halt program execution
SUB A,B ;subtract B from A and store result in A
JZ 6h ;if ALU result is zero, jump to address 6
Data at RAM index 9 = Bh/11d
Data at RAM index 10 = Bh/11d

## Slide 11: Demonstration of the Computer
Assembly Code
MOV A,9h ;move RAM[9] to A
XCHG A,B ;swap A and B
MOV A, Ah ;move RAM[10] to A
SUB A,B ;subtract B from A and store result in A
JZ 6h ;if ALU result is zero, jump to address 6
PUSH B ;Push B to stack
SHR A ;shift logical right A by one bit
HLT ;halt program execution
RAM Index | RAM Content at Index
0 | 0111_1001
1 | 0011_0000
2 | 0111_1010
3 | 0010_0000
4 | 1011_0110
5 | 1100_0000
6 | 0101_0000
7 | 0000_0000
RAM Index | RAM Content at Index
9 | 0000_1011
10 | 0000_1011
Conversion to machine code and mapping
Data Segment
RAM Index | RAM Content at Index
14 | Stack index 1
15 | Stack index 2

## Slide 12: Demonstration of the Computer
Generation of control signals resemble ring counter
Control signal generation occurs at negedge clock
Data transfer occurs at next posedge clock
A=11 at the end of first instruction cycle
MOV A, 9h

## Slide 13: Demonstration of the Computer
XCHG A,B
Initially, A=bh, B=0h
After xchg, A=0h, B=bh

## Slide 14: Demonstration of the Computer
MOV A, Ah
At the end, A=bh

## Slide 15: Demonstration of the Computer
SUB A, B
Initially, A=bh, B=bh
ALU Computes A-B
A=0h

## Slide 16: Demonstration of the Computer
JZ 6h
Zero Flag = 1
Address Field = 6
PC jumps to 6

## Slide 17: Demonstration of the Computer
B sends data to stack
Stack stores that data
SP is decremented
PUSH B

## Slide 18: Demonstration of the Computer
HLT
Program counter value is indefinitely set to 7.
RAM keeps fetching the same instruction